## Slide 1
Team 54: ECEN215 Lab Kit 2
Bi-Weekly Update 4 Gavin Bernard
Maylun Huang
Evan Slyter
Sponsor: John Lusher TA: Hailey Ward
Notes: Michelle

## Slide 2: Project Summary
Problem statement:
Access to an affordable, course-specific solution for distance-learning students to complete ECEN215 Labs is minimal.
Our Solution:
An affordable, self-contained system that enables hands-on measurements and intuitive data displays.
Complete production of labkit for $50-$75
Easily transportable by hand.
AD3: $379
Notes: Kyle

## Slide 3: Integrated System Diagram
Lab Kit System
User’s Breadboard
BLE
BLE
Notes: Eric

## Slide 4: Project Timeline
2/9 | 2/23 | 3/16 | 3/23 | 3/30 | 4/20
Finalize PCB & order Phone-MCU BLE Validation | Soldered backup PCB Begin App Integration | Integrate Signal Gen-App Solder big PCB Integrate Measurement-App | Integration Complete Fully Coded | Final Validation | Final Demo
Notes: Eric

## Slide 5: Power Supply/Signal Generator Gavin Bernard
Accomplishments since last update 25 hrs of effort | Ongoing progress/problems and plans until the next presentation
Fully integrated DC power supply with App and Signal Generator Designed, Soldered, Tested Power Supply on backup PCB | Integrate Signal Generator on backup PCB with App Solder Power Supply and Signal Generator on complete PCB

## Slide 6: Power Supply/Signal Generator Gavin Bernard

## Slide 7: Power Supply Gavin Bernard
Resistor [Ω | Current [mA] | Output Voltage [V] | Power [mW]
30 | 109.33 | 3.28 | 359
20 | 164 | 3.28 | 538
10 | 328 | 3.28 | 1076
5 | 654 | 3.27 | 2,139
3.3 Volt Buck Converter Testing
Resistor [Ω | Current [mA] | Output Voltage [V] | Power [mW]
30 | 166 | 4.97 | 823
20 | 248 | 4.96 | 1,230
10 | 494 | 4.94 | 2,440
5 | 980 | 4.9 | 4,802
5.0 Volt Buck Converter Testing

## Slide 8: Power Supply Gavin Bernard
Resistor [Ω | Current [mA] | Output Voltage [V] | Power [mW]
1,000 | 4.68 | -4.68 | 21.9
500 | 8.82 | -4.41 | 38.9
250 | 16.76 | -4.19 | 70.22
125 | 31.68 | -3.96 | 125.45
-5.0 Volt Charge-Pump Inverter Testing
Variable Voltage Range using App
Input Voltage | Measured Output Voltage [V]
0.1 | 0.1
1 | 0.99
2 | 1.99
3.3 | 3.28
5 | 4.98

## Slide 9: Signal Generator Gavin Bernard
Input | Measured Waveform | Frequency [Hz]
Sine, 1,000 Hz | Sine | 900 Hz
Triangle, 500 Hz | Triangle | 450 Hz
Square, 300 Hz | Square | 280 Hz
Signal Generator using Arduino IDE

## Slide 10: Measurement Subsystem Maylun Huang
Accomplishments since last update 12 hrs of effort | Ongoing progress/problems and plans until the next presentation
Tested code for multimeter inputs, adjusting for internal resistances | On-going soldering parts onto combined PCB On-going mobile app code for multimeter selection

## Slide 11: Measurement Subsystem Maylun Huang
Voltmeter |  | 
Raw Input | Expected | Actual
0.1 | -5 | ~-4.95
1.63 | 0 | ~-0.07
3.23 | 5 | ~4.94

## Slide 12: Measurement Subsystem Maylun Huang
Ohmmeter |  | 
Raw Input | Expected | Actual
3 | 1000 | 1000
2.2 | 5000 | 4950
1.65 | 10000 | 9900

## Slide 13: Measurement Subsystem Maylun Huang
Ammeter |  | 
Raw Input | Expected | Actual
0.32 | 0.1 | 0.083
1.6 | 0.5 | 0.487
3.2 | 1 | 1.01

## Slide 14: Mobile App Evan Slyter
Accomplishments since last update 8 hrs of effort | Ongoing progress/problems and plans until the next presentation
-Power supply fully integrated with app. -Edited lab manual for lab 8. -Verified all commands come across bluetooth successfully. | -Continue integrating subsystems once they’re ready -Commands occasionally not executing on power supply.

## Slide 15: Mobile App Evan Slyter
Commands sometimes not registering
Doesn't seem time based
Hopefully Dev Board issue

## Slide 16: Mobile App Evan Slyter
Lab 8, AND/OR chips need 3 inputs.
Had to add section for voltage dividing.

## Slide 17: Execution Plan
Notes: Michelle

## Slide 18: System Validation Plan
Notes: Michelle

## Slide 19: Questions?